Adjacent Link LLC
Preliminary
DLEP Layer Design
Joseph Giovatto
jgiovatto@adjacentlink.com

---
Overview
Objective
EMANE R2RI Metrics
Peer Discovery
DLEP Modem / DLEP Layer Messages
DLEP Layer Interaction
Flow Diagrams
EMANE DLEP Stack

---
Objective
Develop EMANE DLEP components to allow radio model implementations to directly support DLEP using MIT-LL DLEP Modem API:
Boundary interface for MIT-LL DLEP Modem API that encapsulates any messaging required for peer communication.
Over-the-Air Controller implementing a DLEP destination dynamic discovery protocol.
Develop EMANE DLEP Layer that provides DLEP support for any NEM instantiated with a radio model supporting EMANE R2RI.
DLEP Layer performs R2RI to DLEP metric translation and uses EMANE DLEP components for peer and OTA messaging.

---
R2RI Neighbor Metrics
Metrics pertaining to each Neighbor via EMANE Neighbor R2RI:
NumRxFrames	Number of frames received from the neighbor
NumTxFrames	Number of frames sent to the neighbor
NumMissedFrames	Number of frames missed from the neighbor
BandwidthConsumption	Bandwidth consumption in microseconds
SINRAvg	Average SINR from neighbor in dBm
SINRStd	Standard deviation SINR from neighbor
NoiseFloorAvg	Average noise floor from neighbor in dBm
NoiseFloorStd	Standard deviation noise floor from neighbor
RxAvgDataRate	Average Rx datarate from neighbor bps
TxAvgDataRate	Average Tx datarate to neighbor bps

---
R2RI Self Metrics
Metrics pertaining to the local radio via EMANE Self R2RI:
BroadcastDataRate	Broadcast datarate in bps
MaxDataDataRate	Max datarate in bps
Metrics pertaining to local radio queue(s) via EMANE Queue R2RI:
MaxQueueSize	Max Queue size in bytes
CurrentDepth	Current Queue depth in bytes
NumDiscards	Num packet discards
AvgDelay	Average queue delay in microseconds

---
DLEP Destination Discovery
Problem
DLEP Destinations are defined by an Ethernet MAC Address. In a DLEP Session the MAC Address of the DLEP Router is used in all DLEP Destination related signals. Unfortunately remote nodes have no way of knowing these MAC Address(es) and/or the DLEP Session Up/Down Status at any given time.
Solution
The DLEP Layer tracks the MAC Address of the DLEP Router for all Sessions via the PEER_UP/ PEER_DOWN message. These MAC Address(es) are advertised to all remote destinations via a lossy OTA message at some periodic rate. Upon receipt of these advertisements each DLEP Layer is able to detect new or deleted Destinations and respond with a Destination Up or Destination Down message accordingly.

---
Messages sent from DLEP Layer to DLEP Modem
Triggered by Destination Status Messages:
DEST_UP	indicates detection of a remote DLEP session
Required: macAddress
DEST_DOWN	indicates termination of a remote DLEP session
Required: macAddress
Triggered by Peer Events:
REQUEST_STATUS	in response to request (peer update, link info, etc)
Required RequestId, status

---
Messages sent from DLEP Layer to DLEP Modem cont'd
Triggered by R2RI Messages:
DEST_UPDATE
Required: macAddress
Optional: IPv4/6 address, MDR, CDR, Latency, Resources and RLQ
PEER_UPDATE
Optional: IPv4/6 address, MDR, CDR, Latency, Resources, RLQ
Triggered by Radio Model:
PEER_TERM	indicates radio model termination
Required: macAddress
Optional for Radio Models supporting credits
CREDIT_REQUEST
Required: macAddress
CREDIT_STATUS	in response to a credit grant
Required: macAddress, creditStatus
CREDIT_GRANT	in response to a credit request
Required macAddress, creditAmount

---
Messages sent from DLEP Modem to DLEP Layer
Triggered by Modem/Router Peer activity
PEER_UP	indicates a new local DLEP session
Required: macAddress
PEER_DOWN	indicates termination of a local DLEP session
Required: macAddress
PEER_UPDATE	indicates peer metric changes
Required: macAddress
Optional: IPv4/6 address, MDR, CDR, Latency, Resources and RLQ
PEER_FAIL	indicates local session failure
Required: macAddress, errorCode
Triggered by Peer request
LINK_CHAR_REQ	peer requests specific link characteristics per dest
Required: macAddress
Optional: CDR, Latency
REQUEST_STATUS	in response to a request (peer update, link char req)
Required: MessageId, status

---
Messages sent from DLEP Modem to DLEP Layer cont'd
Optional for Radio Models supporting credits
CREDIT_STATUS	in response to a credit grant
Required: macAddress, creditStatus
CREDIT_GRANT	in response to a credit request
Required: macAddress, creditAmount
CREDIT_REQUEST	request credits per destination
Required: macAddress

---
DLEP Layer Interaction

---
DLEP Peer Event Flow

---
DLEP R2RI Flow

---
DLEP Destination Status Flow

---
DELP/EMANE Component Stack